Model Specification: OnGrip® Spray Traction Surface
Aluminum Metal Fabrication Products

October 21, 2021

Specifier Notes: Architect or engineer should carefully review and edit this section to meet the requirements of the project and local building codes. Coordinate this section with other specification sections and the drawings and delete any unused “Specifier Notes” and options shown in red after editing.

This section covers Ohio Gratings, Inc.’s “Aluminum OnGrip® Spray Traction Surface Products.” Consult Ohio Gratings (www.ohiogratings.com) for assistance in editing this section for specific applications. Call 800.321.9800 or email info@ohiogratings.com with any questions.

SECTION 055000 - Metal Fabrications

Part 1: General

1.1 Section Includes

- OnGrip® Spray Traction Surface on Aluminum Floor Plate.

- OnGrip® Spray Traction Surface on Aluminum Plate Stair Treads.

- OnGrip® Spray Traction Surface on Aluminum Stair Tread Repair Covers.

1.2 Related Requirements

- Section 050523 – Metal Fastenings.

- Section 055100 – Metal Stairs.

- Section 055116 – Metal Floor Plate Stairs.

- Section 055136 – Metal Walkways.

- Section 055400 – Metal Floor Plates.

1.3 Reference Standards

- ANSI A326.3-2017: American National Standard Test Method for Measuring Dynamic Coefficient of Friction of Hard Surface Flooring Materials.

- US Department of Justice: Americans with Disabilities Act (ADA) - 2010 Design Standards: Section 302.1: Slip-resistance.

- ASTM B209: Standard Specification for Aluminum and Aluminum-Alloy Sheet and Plate.

  - Action Submittals

- Product Data: Submit manufacturer’s catalog pages with product data.

- Shop Drawings: Submit manufacturer’s shop drawings, including plans, elevations, sections, and details indicating dimensions, tolerances, materials, components, fabrication, fasteners, hardware, finish, options, and accessories. Show details of attaching traction surface products.

- Samples: Samples of traction surface flooring products shall be submitted for approval (minimum 4” x 4”).

- Manufacturer’s Certification: Submit manufacturer’s certification that materials comply with specified requirements.

  - Quality Assurance

Manufacturer Qualification: A company regularly engaged (for at least 5 years) in the manufacture of traction surface floor plates of similar type to that specified.

  - Delivery, Storage and Handling

- Delivery Requirements: Deliver materials to site in manufacturer’s original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

- Storage and Handling Requirements:

  - Store and handle materials in accordance with manufacturer’s instructions.

  - Keep materials in manufacturer’s original, unopened containers and packaging until installation.

  - Store materials in a clean, dry area indoors.

  - Do not store materials directly on the floor.

  - Store materials on a flat, level surface, raised above the floor and with adequate support to prevent sagging.

  - Protect materials and finish during storage, handling, and installation to prevent damage.

Part 2: Products

2.1 Manufacturers:

OnGrip® Spray Traction Surface, manufactured by Ohio Gratings, Inc. (5299 Southway St. SW, Canton, Ohio 44706, 800-321-9800, www.ohiogratings.com).

2.2 Traction / Slip-Resistance Performance:

Surface shall exceed 0.42 high traction Wet Dynamic Coefficient of Friction (DCOF) requirement of ANSI A326.3-2017 when tested per the standard. OnGrip® Spray Traction Surface meets the American with Disabilities Act (ADA) section 302.1 requirement for slip resistance, and OSHA safety standards.

2.3 Traction Surface Floor Plate:
	Ohio Gratings, Inc. Aluminum “OnGrip® Spray Traction Surface Floor Plate”

- Material: Aluminum ASTM B209; Alloy: 3003 | 5052 | 6061.

- Traction Surface: The OnGrip® Metal Spray Traction Surface process produces a bond strength to the metal substrate exceeding 3,000 psi.

- Plate Thickness: [3/16-inch 4.8mm] | [1/4-inch 6.4mm] [3/8-inch 9.5mm] | [1/2-inch 12.7mm] | [3/4-inch 19mm] | [1-inch 25.4mm] [1- 1/4-inches 32mm] | [1- 1/2-inches 38mm] | [_____].

- Plate Width (maximum 96 inches): [48 inches 1219mm] | [60 inches 1524mm] | [72 inches 1829mm] | [_____].

- Plate Length (maximum 240 inches): [96 inches 2438mm] | [120 inches 3048mm] | [144 inches 3658mm] | [_____].

- Finish: Mill.

- Attachment: as indicated on drawings.

2.4 Traction Surface Plate Stair Treads:

Ohio Gratings, Inc. Aluminum “OnGrip® Spray Traction Surface Plate Stair Treads”

- Material: Aluminum ASTM B209; Alloy: 3003 | 5052 | 6061.

- Traction Surface: The OnGrip® Metal Spray Traction Surface process produces a bond strength to the metal substrate exceeding 3,000 psi.

- Plate Thickness: [3/16-inch 4.8mm] | [1/4-inch 6.4mm] | [_____].

- Tread Depth: [12 inches 305mm] or [_____] (Indicated on drawings).

- Tread Width: [36 inches 914mm] or [_____] (Indicated on drawings).

- Nose Bend Angle: [90 degrees] or [_____] (Indicated on drawings).

- Nose Bend Height: [2 inches 51mm] or [_____] (Indicated on drawings).

- Nose Bend Inside Radius: [7/16-inch 11mm] or [_____].

- Tread Riser Bend Angle: [90 degrees] or [_____] (Indicated on drawings).

- Tread Riser Bend Height: [2 inches 51mm] or [_____] (Indicated on drawings).

- Tread Riser Bend Inside Radius: [7/16-inch 11mm] or [_____].

- Finish: Mill.

- Carrier Attachment: [_____] (Indicated on drawings).

2.5 Traction Surface Stair Tread Repair Covers:

Ohio Gratings, Inc. Aluminum “OnGrip® Spray Traction Surface Stair Tread Repair Covers”

- Material: Aluminum ASTM B209; Alloy: 3003 | 5052 | 6061.

- Traction Surface: The OnGrip® Metal Spray Traction Surface process produces a bond strength to the metal substrate exceeding 3,000 psi.

- Plate Thickness: [3/16-inch 4.8mm] or [_____].

- Tread Depth: [11- 3/4-inches 298mm] or [_____] (Indicated on drawings).

- Tread Width: [35- 3/4-inches 908mm] or [_____] (Indicated on drawings).

- Tread Nose Bend Angle: [90 degrees] or [_____] (Indicated on drawings).

- Tread Nose Bend Height: [1- 1/4-inches 32mm] or [_____] (Indicated on drawings).

- Stair Tread Nose Bend Inside Radius: [7/16-inch 11mm] or [_____].

- Finish: Mill.

- Cover Attachment: [_____] (Indicated on drawings).

Part 3: Execution

3.1 Field Verification:

Examine areas to receive traction surface floor plates or components. Notify project engineer or architect of conditions that would adversely affect installation or subsequent use. Do not begin installation until unacceptable conditions are corrected.

  - Installation

- Install OnGrip® products in accordance with manufacturer’s instructions at locations indicated in the drawings.

- OnGrip® products shall be installed plumb, level, square, straight, accurately aligned, and at the proper elevation as indicated in the drawings.

3.3 Protection:

Protect installed OnGrip® products to ensure that, except for normal weathering, OnGrip® products will be without damage or deterioration at the time of substantial completion.